# Communication specification
Time format: YYYY-MM-DDThh:mm:ss.msec
Every module: Every module is started as a separate process that communicates via stdin and stdout. Every module starts the communication by identifying itself and attempts to let the knowledge module know when it is going to crash or exit while still connected.
Receives:
/central/exit
Sends:
/general/identify (vision|kicker|planner|movement|robot|logger|manual) (primary|secondary) current_time name
name is the name of the module including the version.
A primary module satisfies the requirement of having the module. A secondary module gets the exact same messages but does not satisfy that requirement. Example: the logger.py module should always be there; the visualizer is just good to look at.
/general/exiting reason
Vision module: started with extra parameters side (left|right) and our colour (blue|yellow). All the corrections and normalizations are applied before sending the info (barrel distortion, perspective distortion, our side must always appear to be on the left). See board_specs.png to see how the info relates to the real world.
Sends:
1. /vision/xy (us|enemy|ball) x y frame_time
  1. x and y are real numbers
2. /vision/rotation (us|enemy) r frame_time
  1. r is in radians
Kicker module: uses the robot communication module to kick the ball when ordered to do so by the planning module.
Receives:
1. /planner/kick
2. /planner/lower_kicker
Sends:
/kicker/order/brake
Orders the robot to brake the kicker motor
/kicker/order/run_inf (left|right) speed
Speed is an integer in the range [-128, 127]
Orders the robot to run the kicker motor at the specified speed
Planning module: plans where the robot should move and when it should use the kicker. It does not decide how the robot should achieve the given goals. It will receive all the specified information as soon as it arrives. It will also get all up to 1 minute old information when it first connects to the knowledge module.
Receives:
/vision/*
Sends:
/planner/kick
Kicks the ball as soon as possible
/planner/lower_kicker
Lowers the kicker to the resting position
/planner/move n coordinates (final_rotation|not_important)
n is the number of (x, y) pairs to follow (x and y are real numbers), coordinates = the (x, y) pairs, final_rotation is in radians (backwards movement is allowed if and only if moving to the left)
/planner/move_rev n coordinates (final_rotation|not_important)
same as above but backwards movement is always allowed
Movement module: receives orders to move through a list of points and stop at the last one with a specific rotation if given. If no coordinates are given then the robot must rotate on spot. This module decides which speed to use and can consider the given coordinates to be approximate. It will receive all the specified information as soon as it arrives. It will also get all up to 1 minute old information when it first connects to the knowledge module. A newer move order overrides the old one.
Receives:
1. /vision/* (only our location)
2. /planner/move
3. /planner/move_rev
4. /movement/order/*
5. /kicker/order/*
Robot communication module: communicates with the robot over Bluetooth. Sends and receives data as ordered by the sensor, movement and kicker modules.
Receives:
1. /vision/*
2. /planner/move
3. /planner/move_rev
4. /movement/order/*
5. /kicker/order/*
Logging module: receives all messages passing through the knowledge module with some additional info as specified below. The main logger should be connected at all times but there may be additional loggers attached (for example a visualizer). It will also get all up to 1 minute old information when it first connects to the knowledge module.
Receives:
1. /central/received_message
2. /central/sent_message
Proxy module: sits between the knowledge module and every other module. It will execute the program specified in its arguments and then communicate with the knowledge module using TCP/IP and with the end module using stdio. It will pass on every message without modifications or trying to understand them. It will intercept the /exit message and kill the process if it doesn’t do that by itself.
Receives:
Any message its end module is supposed to receive
Sends:
1. Any message its end module is supposed to send
2. /general/crashed reason
Sent if the end module crashes
Central server: the central module that makes sure every other module is running and passes messages between them.
Receives:
/general/*
Sends:
1. Messages it receives that should be redirected to other modules
2. /central/received_message (vision|kicker|planner|movement|robot|logger|manual|central|unknown) client_id receiving_time the_message
client_id is a unique integer given to a connected client module.
/central/sent_message (vision|kicker|planner|movement|robot|logger|manual|central|unknown) client_id sending_time the_message
client_id is a unique integer given to a connected client module.
/central/exit
The module it is sent to must exit cleanly